## Slide 1
NVIDIA's Improvements to RISC-V
1
1. At the Microarchitecture Level (Comparison with Falcon)
• Upgraded Branch Prediction Mechanism:
  The old version of Falcon only used static prediction. NV-RISC-V introduces dynamic prediction mechanisms, including BTB(Branch Target Buffer), BHT(Branch History Table), and RAS(Return Address Stack), significantly reducing performance losses caused by branch prediction errors.
Notes: 透明度与信任
实现完全透明的关键障碍是什么？
透明度服务如何增强安全性和可信度？
透明度注册机构如何提供可靠的日志？

## Slide 2
NVIDIA's Improvements to RISC-V
2
1. At the Microarchitecture Level (Comparison with Falcon)
• Instruction Execution and Pipeline Optimization:
  When handling instruction hazards, Falcon can only resolve them through Stall, while NV-RISV introduces ROB to handle WAW hazards, enabling out-of-order execution.
• Memory Protection Mechanism:
  Upgraded from Falcon's simple TCM tagging to a more flexible Base and Boundmechanism, and introduced MPU (Memory Protection Unit).
Notes: 透明度与信任
实现完全透明的关键障碍是什么？
透明度服务如何增强安全性和可信度？
透明度注册机构如何提供可靠的日志？

## Slide 3
NVIDIA's Improvements to RISC-V
3
2. Hardware Acceleration for AI and Computationally Intensive Tasks
• Ultra-Wide Vector Extension:
  NV-RVV cores, in addition to standard RISC-V... Building upon this foundation, a 1024-bit vector extension width has been added, far exceeding the configuration of typical embedded cores, specifically for high-throughput vector operations.
Notes: 透明度与信任
实现完全透明的关键障碍是什么？
透明度服务如何增强安全性和可信度？
透明度注册机构如何提供可靠的日志？

## Slide 4
NVIDIA's Improvements to RISC-V
4
2. Hardware Acceleration for AI and Computationally Intensive Tasks
• Deep Learning Dedicated Module Integration:
  In the Deep Learning Accelerator (DLA), the RISC-V core is tightly coupled with several dedicated hardware modules, including Rubik (matrix transformation optimization module), SDP (scaling and dynamic precision processing module), and CfgDMA (configurable DMA).CDP (compression and decompression module) is integrated to optimize data stream transmission.
Notes: 透明度与信任
实现完全透明的关键障碍是什么？
透明度服务如何增强安全性和可信度？
透明度注册机构如何提供可靠的日志？

## Slide 5
NVIDIA's Improvements to RISC-V
5
3. System-Level Interconnect and Security Architecture Improvements
• IOPMP (Input-Output Memory Protection):
    NVIDIA has developed and contributed the IOPMP technology, which provides protection when I/O devices access memory. This is crucial in GSP (GPU System Processor), as it ensures strict resource isolation and security protection between guest virtual machines (Guest VMs) of different users in a multi-tenant cloud environment.
Notes: 透明度与信任
实现完全透明的关键障碍是什么？
透明度服务如何增强安全性和可信度？
透明度注册机构如何提供可靠的日志？

## Slide 6
NVIDIA's Improvements to RISC-V
6
3. System-Level Interconnect and Security Architecture Improvements
• Unified Secure Debugging:
    The security of the debug interface has been improved, integrating the ICD (In-Circuit Debug) secure debugging function and combining it with ROM memory protection to prevent physical attacks via the debug interface.
Notes: 透明度与信任
实现完全透明的关键障碍是什么？
透明度服务如何增强安全性和可信度？
透明度注册机构如何提供可靠的日志？

## Slide 7
NVIDIA's Improvements to RISC-V
7
4. In-Depth Customization of Compiler and Software Stack
• Compiler Node Fusion:
    The compiler for DLA (Deep Learning Accelerator) has been enhanced to integrate multiple compute nodes into a single RVV (RISC-V Vector Extension) kernel. This means the compiler can automatically identify computational steps that can be merged, reducing kernel launch overhead and optimizing hardware computing efficiency
Notes: 透明度与信任
实现完全透明的关键障碍是什么？
透明度服务如何增强安全性和可信度？
透明度注册机构如何提供可靠的日志？

## Slide 8
NVIDIA's Improvements to RISC-V
8
4. In-Depth Customization of Compiler and Software Stack
• High-Security Language Support:
    To meet extremely high security standards, NVIDIA has adopted Ada/Spark compiler technology from AdaCore, which is used to implement high-security RISC-V firmware development and compiler certification
Notes: 透明度与信任
实现完全透明的关键障碍是什么？
透明度服务如何增强安全性和可信度？
透明度注册机构如何提供可靠的日志？